ROBUST STUDY SUMMARY - Persistence

| Item | Yes | No |
| --- | --- | --- |
| Reference: USEPA HPV Robust Summary. FND Ether Amines Category HPV Chemicals Challenge. 201-14978. December 29, 2003 |
| Test Substance CAS # and name (specify, but do not assess this item): 124-30-1; Octadecylamine |
| Substance purity reported? (Y/N and specify) >99% primary amines | X |  |
| Method |
| References (Y/N) | X |  |
| OECD, EU, national, or other standard method? (Y/N) OECD 301F | X |  |
| If not a standard method, justification of the method/protocol provided? (Y/N) | n/a |  |
| Test design / conditions |
| Study type (e.g., hydrolysis, biodegradation, etc. – specify, but do not assess): biodegradation |
| Conditions type (aerobic or anaerobic - specify, but do not assess): aerobic |
| Test medium (air, water, soil, or sediment - specify, but do not assess): water |
| Information on stability of the substance in the media of concern available? (do not assess this item) No |
| Information on controls (Y/N and specify, positive or negative) positive & negative | X |  |
| Number of replicates (Y/N and specify) 2 | X |  |
| Temperature (Y/N and specify) 20 +/- 1 degree C | X |  |
| Test duration (Y/N and specify) 28 days | X |  |
| Analytical method / technique used (Y/N) | X |  |
| For photodegradation only |
| Reactants of gas-phase reactions (specify, but do not assess this item) |
| Light source (Y/N and specify) |  |  |
| Light spectrum and/or relative intensity based on sunlight intensity (Y/N) |  |  |
| For hydrolysis only |
| Measured concentrations reported? (Y/N) |  |  |
| pH values reported? (Y/N and specify) |  |  |
| For biodegradation only |
| Ready or inherent biodegradation? (specify, but do not assess this item) Ready |
| Substance concentration (Y/N) | X |  |
| Inoculum source (Y/N) | X |  |
| Inoculum concentration or number of microorganisms (Y/N) |  | X |
| Results |
| Endpoints / values / units (do not assess this item): 70% after 28 days |
| Information on breakdown products available? (do not assess this item) No |
| Overall score: 10/11= 91% |
| EC Reliability code: 1 |
| Reliability category (high, satisfactory, low): High |
| Comments: |